## Slide 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 6 | Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 14 Minutes | 58 | 64 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Florian::Holzbauer, Markus::Maier, Johanna::Ullrich | | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ff05::IMC24 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 128 | 0 | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identifier | Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination Reachable: | What ICMPv6 Error Messages Reveal
| About Their Sources
+-+-+-+-+-

## Slide 2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 6 | Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload Length | 58 | 64 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:5ba::1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:200::random IID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 128 | 0 | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identifier | Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Echo Request
+-+-+-+-+-
1
Sending a request to every IPv4 address takes less than an hour
Scanning every address not feasible in IPv6
ICMPv6 error messages are still returned, even when targeting a random address inside a network
Notes: ICMPv6 error messages are part of the ICMPv6 protocol, which is an integral part of IPv6 and MUST be implemented by every IPv6 node
It is responsible for reporting errors in processing packets and diagnostics.
Everyone of you is probably familiar with PING,
- it is the process of sending an echo request and in case of a successful connection we will receive an echo reply, however in case of an error we can receive one of the following errors:

## Slide 3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 6 | Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload Length | 58 | 56 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:200:1000::ab |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:5ba::1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 1 | 0 | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identifier | Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination Unreachable
+-+-+-+-+-
🧐
Typ | Error Message | Codes | Level
1 | Destination Unreachable | 7 | SHOULD
2 | Packet Too Big | 1 | MUST
3 | Time Exceeded | 2 | MUST
4 | Parameter Problem | 3 | SHOULD
Code 0 infers?
2
Notes: ICMPv6 currently defines 4 different error message types.
In this work the scope lays on Destination Unreachable and Time Exceeded that are returned in response to packets with valid headers and do not exceed the MTU
They have different requirement levels. Destination Reachable should be returned to the sender

## Slide 4
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 6 | Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload Length | 58 | 56 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:200:1000::ab |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:5ba::1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 1 | 0 | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identifier | Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination Unreachable
+-+-+-+-+-
🧐
Code 0 infers?
Code | Description
0 | No route to destination
1 | Communication with destination administratively prohibited
2 | Beyond scope of source address
3 | Address unreachable
4 | Port unreachable
5 | Source address failed ingress/egress policy
6 | Reject route to destination
3
Notes: 0) No entry in routing table for dest. ip
Firewalling
2) Beyond scope =
3) Address Unreachable, no other code matches and mainly if link-local address cannot be resolved
4) Dest. Host has no listener
5) Source based filtering
6) Router has been configured to reject all the traffic for a specific destination prefix (Null Routing)

## Slide 5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 6 | Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload Length | 58 | 56 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:200:1000::ab |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:5ba::1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 3 | 0 | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identifier | Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time Exceeded
+-+-+-+-+-
🧐
Typ | Error Message | Codes | Level
1 | Destination Unreachable | 7 | SHOULD
2 | Packet Too Big | 1 | MUST
3 | Time Exceeded | 2 | MUST
4 | Parameter Problem | 3 | SHOULD
Routing Loop!!
4

## Slide 6
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 6 | Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload Length | 58 | 56 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:200:1000::ab |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:5ba::1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 1,3 | Code | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identifier | Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ICMPv6 Error Message
+-+-+-+-+-
🧐
Periphery Addresses
Error Messages in Measurements
Edgy (Rye, 2020)
  64.8M Last-Hop Routers
XMap (Li, 2021)
  52M Routers + User Equipment (15 ISP ranges)
Periphery can include your:
  Home Router
  Smartphone
5

## Slide 7
Our Goal:
Analyze ICMPv6 error messages beyond their source addresses
  Our Contribution:
    1. Verification of error message type & code usage and classification of error messages for 11 Billion IPv6 prefixes
    2. ICMPv6 error message rate-limiting measurements of 1.4M routers show vendor defaults & kernel versions
6
Active network behind router
Device Information

## Slide 8: What Do ICMPv6 Error Messages Reveal About Their Sources?
Networks
2. Routers
7
Notes: Slides in the layout KAPITEL/TRENNfolie (main part of the presentation, in contrast to the blue COVER slide) are generally in BLUE colour. Special slides, such as the quote or message slide are held in dark red, dark green or dark grey.

## Slide 9: Methods Overview
Controlled Environment
2. Verification in the IPv6 Internet
3. IPv6-wide Measurements
8
Collect error messages under six different routing scenarios
Find error messages that are returned only for active/inactive networks

## Slide 10: Router Lab
Typ | Firewall
1 | PfSense
2 | Fortigate
sbaresearch/router-lab
Routed
11 Vendors, 15 Appliances, 6 routing scenarios derived from RFC 4443
Valuable for further reconnaissance
9
Typ | Router / Router OS
1 | Cisco XRv, IOS-XE, IOS
2 | Juniper Junos
3 | Huawei NetEngine
4 | HPE VSR
5 | Arista
6 | VyOs
7 | Mikrotik (2 Versions)
8 | OpenWRT (2 Versions)
9 | Aruba

## Slide 11: Result I: Router Lab
Scenario | 1 | 2 | 3 | 4 | 5 | 6 | 
Description | Active Network | Inactive Network | Active Netw. ACL | Inactive Netw. ACL | Null Route | Routing Loop | Classification
No Route (S2) | ○ 0 | ● 14 | ● 1 | ● 2 | ● 2 | ○ 0 | Ambiguous
Admin. Prohib. (S3,S4) | ○ 0 | ○ 0 | ● 4 | ● 5 | ● 3 | ○ 0 | Ambiguous
Addr. Unreach. (S1) | ● 14 | ○ 0 | ○ 0 | ○ 0 | ● 1 | ○ 0 | Ambiguous
Port Unreach. () | ○ 0 | ○ 0 | ● 3 | ● 2 | ○ 0 | ○ 0 | Ambiguous
Failed Policy (S3,S4) | ○ 0 | ● 1 | ● 1 | ● 2 | ○ 0 | ○ 0 | Ambiguous
Reject Route (S5) | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 2 | ○ 0 | Inactive
Time Exceeded (S6) | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 15 | Inactive
∅ | ● 1 | ○ 0 | ● 4 | ● 3 | ● 9 | ○ 0 | 
Mikrotik
10
Notes: Controlled environment, limited number vendors but full control of the routers.
Klassifizierung: Active, inactive, ambiguous + Timing Unterschied

## Slide 12: Result I: Router Lab
Scenario | 1 | 2 | 3 | 4 | 5 | 6 | 
Description | Active Network | Inactive Network | Active Netw. ACL | Inactive Netw. ACL | Null Route | Routing Loop | Classification
No Route (S2) | ○ 0 | ● 14 | ● 1 | ● 2 | ● 2 | ○ 0 | Ambiguous
Admin. Prohib. (S3,S4) | ○ 0 | ○ 0 | ● 4 | ● 5 | ● 3 | ○ 0 | Ambiguous
Addr. Unreach. (S1) | ● 14 | ○ 0 | ○ 0 | ○ 0 | ● 1 | ○ 0 | Ambiguous
Port Unreach. () | ○ 0 | ○ 0 | ● 3 | ● 2 | ○ 0 | ○ 0 | Ambiguous
Failed Policy (S3,S4) | ○ 0 | ● 1 | ● 1 | ● 2 | ○ 0 | ○ 0 | Ambiguous
Reject Route (S5) | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 2 | ○ 0 | Inactive
Time Exceeded (S6) | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 15 | Inactive
∅ | ● 1 | ○ 0 | ● 4 | ● 3 | ● 9 | ○ 0 | 
Juniper
11
Solution: RTTs! AU in S1 shows delays of 2, 3 and 18 seconds, in S5 it is returned immediately
Notes: Controlled environment, limited number vendors but full control of the routers.
Klassifizierung: Active, inactive, ambiguous + Timing Unterschied

## Slide 13: Result I: Router Lab
Scenario | 1 | 2 | 3 | 4 | 5 | 6 | 
Description | Active Network | Inactive Network | Active Netw. ACL | Inactive Netw. ACL | Null Route | Routing Loop | Classification
No Route (S2) | ○ 0 | ● 14 | ● 1 | ● 2 | ● 2 | ○ 0 | Ambiguous
Admin. Prohib. (S3,S4) | ○ 0 | ○ 0 | ● 4 | ● 5 | ● 3 | ○ 0 | Ambiguous
Addr. Unreach.RTT≥1sec | ● 14 | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ○ 0 | Active
Addr. Unreach.RTT<1sec | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 1 | ○ 0 | Inactive
Port Unreach. () | ○ 0 | ○ 0 | ● 3 | ● 2 | ○ 0 | ○ 0 | Ambiguous
Failed Policy (S3,S4) | ○ 0 | ● 1 | ● 1 | ● 2 | ○ 0 | ○ 0 | Ambiguous
Reject Route (S5) | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 2 | ○ 0 | Inactive
Time Exceeded (S6) | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 15 | Inactive
∅ | ● 1 | ○ 0 | ● 4 | ● 3 | ● 9 | ○ 0 | 
12
Notes: Controlled environment, limited number vendors but full control of the routers.
Klassifizierung: Active, inactive, ambiguous + Timing Unterschied

## Slide 14: Result I: Classification
Scenario | 1 | 2 | 3 | 4 | 5 | 6 | 
Description | Active Network | Inactive Network | Active Netw. ACL | Inactive Netw. ACL | Null Route | Routing Loop | Classification
No Route (S2) | ○ 0 | ● 14 | ● 1 | ● 2 | ● 2 | ○ 0 | Ambiguous
Admin. Prohib. (S3,S4) | ○ 0 | ○ 0 | ● 4 | ● 5 | ● 3 | ○ 0 | Ambiguous
Addr. Unreach.RTT≥1sec | ● 14 | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ○ 0 | Active
Addr. Unreach.RTT<1sec | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 1 | ○ 0 | Inactive
Port Unreach. () | ○ 0 | ○ 0 | ● 3 | ● 2 | ○ 0 | ○ 0 | Ambiguous
Failed Policy (S3,S4) | ○ 0 | ● 1 | ● 1 | ● 2 | ○ 0 | ○ 0 | Ambiguous
Reject Route (S5) | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 2 | ○ 0 | Inactive
Time Exceeded (S6) | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ○ 0 | ● 15 | Inactive
∅ | ● 1 | ○ 0 | ● 4 | ● 3 | ● 9 | ○ 0 | 
13
Notes: Controlled environment, limited number vendors but full control of the routers.
Klassifizierung: Active, inactive, ambiguous + Timing Unterschied

## Slide 15: Methods Overview
Controlled Environment
2. Verification in the IPv6 Internet
3. IPv6-wide Measurements
14
Goal: Collect error messages for IPv6 networks known to be active and inactive
Problem: There is no such dataset
  Scanning random subnets?
    Target network might not be suballocated
BValue Steps = Border Values to the rescue

## Slide 16: BValue Steps
Applied to one hitlist address/subnet per routed BGP prefix
47,923 pass ICMPv6 responsiveness check
We are able separate active from inactive in 44% (17% are not suballocated, 38% unresponsive)
  Input: Responsive IPv6 addresses in active network (Hitlist Service; Gasser, 2018)
Randomize more and more of the target address (steps of 8 bits) up to the routed network border
Detect changes in response behavior
  Active = before change
  Inactive = after change
15
Hitlist IP
B127​
B120​
...
.
B32
Unassigned IPs
Active
Inactive

## Slide 17: Result II: BValue Steps
True Positives
True Negatives
16
Of error messages for active networks
Five days, Three protocols
95% labeled active networks returned AURTT≥1sec
80% labeled inactive networks returned AURTT<1sec, Reject Route, Time Exceeded; 16% Ambiguous (Higher share of No Route)
Error Messages
BValues
18,250/21,070 Responsive
10,346/21,070 Responsive
Notes: False Negatives: Publicly available loopback-interfaces

## Slide 18: Methods Overview
Controlled Environment
2. Verification in the IPv6 Internet
3. IPv6-wide Measurements
17

## Slide 19: IPv6-wide measurements
  YARRP (Beverly, 2016): Traceroutes to 5 Billion /48s:
  ZMap (Gasser, 2016) Scans to 6 Billion /64s:
HL: 2
HL: 3
Time Exceeded
Time Exceeded
Time Exceeded
HL: 4
Dest. Unreach. Time Exceeded
HL: 1
HL: 255
Random IID
Dest. Unreach.
Time Exceeded
Router Addr, Hop Count & Destination IP = Input for Contribution 2
18

## Slide 20: Result III: /64s Measurement
Measured /64s | 6,085,410,816 (100%)
Responsive | 1,368,371,825 (22.5%)
Unresponsive | 4,717,038,991 (77.5%)
Responsive | /64s
Active | 355,616,627 = 26%
Ambiguous | 209,970,342 = 15%
Inactive | 802,784,856 = 59%
38% of measured networks remain silent
At least 1 active /64 in 61% of responsive networks
19
Only 15% of responsive /64s remain ambiguous

## Slide 21: What Do ICMPv6 Error Messages Reveal About Their Sources?
Networks
2. Routers
20
Notes: Slides in the layout KAPITEL/TRENNfolie (main part of the presentation, in contrast to the blue COVER slide) are generally in BLUE colour. Special slides, such as the quote or message slide are held in dark red, dark green or dark grey.

## Slide 22: Methods Overview
Controlled Environment
Origination of ICMPv6 error messages must be rate limited
Measure & detect rate limits that are unique to vendors
21
Refill Size
Refill Interval (ms)
Bucket Size
X
… Token
1 Token removed per error message

## Slide 23: Methods Overview
Controlled Environment
Origination of ICMPv6 error messages must be rate limited
Measure & detect rate limits that are unique to vendors
21
Requests
Refill Size
Refill Interval (ms)
Bucket Size
X
… Token
1
1 Token removed per error message
10 sec
x
IP behind router
...
Target Router

## Slide 24: Methods Overview
Controlled Environment
Origination of ICMPv6 error messages must be rate limited
Measure & detect rate limits that are unique to vendors
NR(10) … Total error messages over timespan of 10 seconds
T1, T2, T10 Number of error messages during 1st, 2nd, .. 10th second
21
T1 | T2 | T3 | … | T10
Requests
Refill Size
Refill Interval (ms)
Bucket Size
X
… Token
1
1 Token removed per error message
10 sec
x
IP behind router
...
NR, AU, TX
Target Router

## Slide 25: Result I: Router Lab
Vendor Defaults
Kernel Defaults
22

## Slide 26: Result I: Changes in the Kernel
Number of error messages over 10 seconds
Static and dynamic testing of the Linux kernel shows a change for IPv6 in kernel version 4.
Three rate-limiting changes over time:
Introduction of global rate
Peer-based becomes adaptive to dest. prefix
Global bucket is randomized
23

## Slide 27: Methods Overview
2. Verification in the IPv6 Internet
Our Goal:
  1) Validate collected defaults in the Internet
  2) Extend defaults with new rate-limits for which the vendor is known (see Paper)
Data Source:
  Extract SNMPv3 vendor labels for 476K IPv6 routers (Albakour, 2021)
  50,952 match our tracerouting data, for which we can collect rate limit parameters
      requires:
24
destination behind router, hop limit

## Slide 28: Result II: SNMPv3 Label Comparison
Huawei labeled match lab default
Cisco labeled match XRv and IOS lab defaults
Majority of Juniper labeled is limited above measurement scanrate of 200pps
Mikrotik matches Linux kernel defaults
25

## Slide 29: Methods Overview
3. IPv6-wide Measurements
We collected rate-limits for 1.4M of the IPv6 routers
  Split Routers based on Centrality Score:
    Number of paths to a /48 destination a router is seen on
  Distance-based matching to known rate limiting paramters
    Bin the number of responses for each second (T1,T2,..T10) and compute distance
    Match rate limiting parameters (Bucket Size, Refill Interval, Refill Size) for rates within adaptive threshold (10 to 100 based on NR(10))
  Measurement Parameters: 200 PPS, 10 seconds, Time Exceeded
26

## Slide 30: Result III: Rate Limit Matching
Routers on multiple paths (green), more distinguishable rate limits
  E.g. Cisco (18% IOS, 4.2% XRv)
Periphery (purple)
  83.4% Linux <4.9 or newer version with small dest. prefix sizes (less likely)
  12.6% ≥4.19 with default route
27

## Slide 31: Conclusion: What Do ICMPv6 Error Messages Reveal About Their Sources?
Networks
2. Routers
+ Active
  AURTT≥ 1 sec
+ Inactive
  RR, TX & AURTT<1sec
+ Centrality > 1:
  Vendors
+ Centrality = 1:
  Kernel Version
28
Notes: Slides in the layout KAPITEL/TRENNfolie (main part of the presentation, in contrast to the blue COVER slide) are generally in BLUE colour. Special slides, such as the quote or message slide are held in dark red, dark green or dark grey.

## Slide 32
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 6 | Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload Length | 58 | 56 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:200:1000::ab |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 2001:db8:5ba::1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 129,1,3 | Code | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identifier | Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Questions?
| … Please set Typ and Code accordingly :)
+-+-+-+-+-
Dipl.-Ing. Florian Holzbauer
PhD Candidate @University of Vienna
florian.holzbauer@univie.ac.at
Artifacts available:
sbaresearch/icmpv6-destination-reachable
sbaresearch/router-lab