## Slide 1
Tracking Internet Disruptions in Ukraine: Insights from Three Years of Active Full Block Scans
Florian Holzbauer, Sebastian Strobl & Johanna Ullrich

## Slide 2: Motivation
Since then every 2h
$ countrymonitor/scan.sh UA 8000
FEBRUARY2022
FEBRUARY
2025
Assumption: Internet-connected devices serve as sensors
02-23
02-24
02-03 10:00
[Guardian]
[New York Times]

## Slide 3: From Austria to Ukraine and back
🖥️ 10.5 Million Requests
📦 8,000 Packets per Second
⏰ 22 Minutes Scan Duration
🖥️ ⌀ 1.5 Mio Responses every 2h
🗣️ 1 Opt-Out Notification

## Slide 4: From Ping to Outage Signal
Timestamp | /24 | 
2022-03-02 10:00 | 193.151.240 | ✅
2022-03-02 12:00 | 193.151.240 | ❌
2022-03-02 14:00 | 193.151.240 | ✅
Timestamp | IP | /24
2022-03-02 10:00 | 193.151.240.1 | 193.151.240
2022-03-02 10:00 | 193.151.240.112 | 193.151.240
2022-03-02 10:00 | 193.151.240.13 | 193.151.240
2022-03-02 10:00 | 193.151.240.15 | 193.151.240
2022-03-02 14:00 | 193.151.240.1 | 193.151.240
2022-03-02 14:00 | 193.151.240.112 | 193.151.240
2022-03-02 14:00 | 193.151.240.15 | 193.151.240
Org.
Region
1. IPs to /24 blocks
2. Block attribution with external datasets

## Slide 5: From Ping to Outage Signal
🟢 Active /24s
/24 Block
/24 Block
🔴 Responsive IPs
🔵 Routed /24s
193.151.240​
193.151.241
.241.1
.240.201
.240.101
⚠️ Outage = current Value < X% of moving average of previous week
UPDATE 193.151.240/24 AS1
AS1
AS2
2. ❌ Link Fehler
BGP Feeds
3. UPDATE WITHDRAW
...

## Slide 6: 8 Insights from Tracking Internet Disruptions in Ukraine
Kherson
Kyiv
Lviv

## Slide 7
 | Singla et al. | Klick et al. | IODA
Protocols | Modbus, DNP3 | 60+ | ICMP
Signal | IP based | IP based | Block based (Sampling)
Interval | 24 Hours | 4 Hours | 10 Minutes
War Coverage | 6 Months 2022 | Until March 2023 | Since 2022
Outage Location | IP Geolocation | Static IPs | IP Geolocation
Limited war coverage
Static IPs only?
Sampling?
Geolocation Precision?
Signal differences?
Short-lived outages?
#1 Existing measurements fail to comprehensively track disruptions in Ukraine.
Trinocular

## Slide 8
IODA returns raw data for 90% of ASes (1,597 out of 1,773) but only reports outages for 19% (333) of ASes.
#2 We report outages for many smaller ASes in Ukraine while IODA does not.
Figure 2: Outages reported for 1,773 ASes with regional /24s in Ukraine.

## Slide 9
33%
Figure 3: IP Churn - Comparing 2022 with 2025
3.7M IPs affected
40% to other countries (1.5M IPs)
60% between oblasts
Ukrtelecom, Kyivstar, Vodafone, Vega
#3 Significant IP churn visible in Ukraine, especially in frontline regions.
Notes: Wie sieht die Umfrage genau aus?
Ziele: keinesfalls die Infrastruktur in einem Land mit Krieg belasten (Ziel erreicht: eine einzige Opt-Out Meldung und
Wir messen die Zeit die ein Paket von Österreich in die Ukraine braucht und zurück
Wir messen ob das Ziel antwortet oder nicht
X Anfragen pro Tag
~ X Antworten pro Tag
Aus ethischen Gründen keine Zielnetzwerke überlasten
-> ICMP -> kleinen Fußabdruck bewahren
-> Alle 2h
-> 8000 Pakete pro Sekunde (480 KB/s)

## Slide 10
Challenge:
Assign outages to a region in Ukraine
Kherson
Kyiv
Lviv
Timestamp | /24 | 
2022-03-02 10:00 | 193.151.240 | ✅
2022-03-02 12:00 | 193.151.240 | ❌
2022-03-02 14:00 | 193.151.240 | ✅
#4 Regional classification detects long-term trends in geolocation.
Regional Classification: Only consider /24s that have more than M addresses in the target region for more than T_perc of routed months.
In the paper: M = T_perc = 70%

## Slide 11
Class | Kherson |  | 
 | ASNs | IPs | /24s
Total | 118 | 73.8K | 512
Regional | 13 | 8.3K | 33
Non-Regional | 40 | 65K | 465
Target Set | 34 | 41.7K | 168
Kherson
Identifies 32% of blocks for which outages are representative of the Kherson region
Target set serves as input to outage detection.
#4 Regional classification detects long-term trends in geolocation.

## Slide 12
Intense attacks on the power grid -> partial outages through IPS signal
  Infrastructure types (core vs edge)
Full block outages (FBS) more frequent in frontline regions
Only part of the outages are passively visible in BGP
#5 Internet disruptions in Ukraine peaked during winter 2022/23 and throughout 2024.
Figure 5: Outages detected by each signal type across oblasts.
Notes: 26 Verwaltungseinheiten = Oblaste
Cherkasy 66720.0
Chernihiv 16094.0
Chernivtsi 25836.0
Crimea 21274.0
Dnipropetrovsk 110736.0
Donetsk 58501.0
Ivano-Frankivsk 31113.0
Kharkiv 125910.0
Kherson 19649.0
Khmelnytskyi 54904.0
Kirovohrad 19542.0
Kyiv 622087.0
Luhansk 24089.0
Lviv 89439.0
Mykolaiv 37307.0
Odessa 115518.0
Poltava 61278.0
Rivne 29108.0
Sumy 25549.0
Ternopil 42407.0
Transcarpathia 16639.0
Vinnytsia 49883.0
Volyn 19089.0
Zaporizhzhia 56995.0
Zhytomyr 21131.0

## Slide 13
Figure 7: Average number of 2h intervals with outages.
#6 Difference between frontline and non-frontline unique to our dataset.
Notes: 26 Verwaltungseinheiten = Oblaste
Cherkasy 66720.0
Chernihiv 16094.0
Chernivtsi 25836.0
Crimea 21274.0
Dnipropetrovsk 110736.0
Donetsk 58501.0
Ivano-Frankivsk 31113.0
Kharkiv 125910.0
Kherson 19649.0
Khmelnytskyi 54904.0
Kirovohrad 19542.0
Kyiv 622087.0
Luhansk 24089.0
Lviv 89439.0
Mykolaiv 37307.0
Odessa 115518.0
Poltava 61278.0
Rivne 29108.0
Sumy 25549.0
Ternopil 42407.0
Transcarpathia 16639.0
Vinnytsia 49883.0
Volyn 19089.0
Zaporizhzhia 56995.0
Zhytomyr 21131.0

## Slide 14
IODA: Frontline and Non-Frontline regions show similar behavior
#6 Difference between frontline and non-frontline unique to our dataset.
Figure 7: Average number of 2h intervals with outages.
Notes: 26 Verwaltungseinheiten = Oblaste
Cherkasy 66720.0
Chernihiv 16094.0
Chernivtsi 25836.0
Crimea 21274.0
Dnipropetrovsk 110736.0
Donetsk 58501.0
Ivano-Frankivsk 31113.0
Kharkiv 125910.0
Kherson 19649.0
Khmelnytskyi 54904.0
Kirovohrad 19542.0
Kyiv 622087.0
Luhansk 24089.0
Lviv 89439.0
Mykolaiv 37307.0
Odessa 115518.0
Poltava 61278.0
Rivne 29108.0
Sumy 25549.0
Ternopil 42407.0
Transcarpathia 16639.0
Vinnytsia 49883.0
Volyn 19089.0
Zaporizhzhia 56995.0
Zhytomyr 21131.0

## Slide 15
Avg. 686 HOURS Max. 2822 HOURS with Internet outages in 2024
1951 HOURS with electricity outages in 2024
Pearson r=0.725 overlap of days
#7 Strong correlation of days with outages & power cuts in non-frontline regions.
Figure 8: Hours affected by power and Internet outages in 2024.

## Slide 16: Kherson – 3 Years on the Frontline
Kherson
Notes: Siedlungen städtischen Typs: 31
Dörfer: 656
Siedlungen: 88

## Slide 17
#8 Dataset provides insights into smaller regional providers in Kherson.

## Slide 18
Incident: Russian soldiers search
STATUS Office
CountryMonitor: Decline in responsive IPs for ASN 25482 (STATUS ISP) at the same time as the incident
#8 Dataset provides insights into smaller regional providers in Kherson.

## Slide 19: Nov 2022: Kherson city powered through generators
Kherson
Kyiv
⚡ Daily Cycles
START: 08:00
END: 18:00
Russian Troops destroy critical infrastructure (TV Tower, Heat/Power Plant during retreat )
ISP "STATUS"
#8 Dataset provides insights into smaller regional providers in Kherson.

## Slide 20: Jun/2023 Kakhovka Dam
Ostrov Net AS6446
#8 Dataset provides insights into smaller regional providers in Kherson.

## Slide 21: CountryMonitor - Takeaways
 | Singla et al. | Klick et al. | IODA | CountryMonitor
Protocols | Modbus, DNP3 | 60+ | ICMP | ICMP
Signal | IP based | IP based | Block based (Sampling) | Block based (no Sampling)
Interval | 24 Hours | 4 Hours | 10 Minutes | 2 Hours
War Coverage | 6 Months 2022 | Until March 2023 | Since 2022 | Since 2022
Outage Location | IP Geolocation | Static IPs | IP Geolocation | Regional Classification
Short-lived outages >= 2h
Static IPs only? ✅
Sampling? Small Providers✅
Geolocation Precision ✅

## Slide 22
Acknowledgements:
Alexander Kovalenko – Status ISP
Dipl.-Ing. Florian Holzbauer
Researcher & PhD Candidate
University of Vienna
florian.holzbauer@univie.ac.at
countrymonitor.github.io Research Access -> Oct 28th​ 2025